ID	Group	Name	Return	Parameter	Annotations/Description
0	Tasking	execute	error	path	Executes the executable at path
1		createThread	uint32_t	Void (*)(), priority (int)	Executes the function given in a separate thread with the specified priority. Returns the ID of the new task
2		exit			Exits from the current thread/task
3		wait	bool	Reason, data, timeout	Locks a task until the timeout is reached (return false) or the reason for the block has gone
4		createConsoleThread	uint32_t	Void (*)(), priority (int), name	Executes the function given in a separate thread with the specified priority in a new console. Returns the ID of the new task
5
6		getMyPID	uint32_t		Returns the ID of the current process
7
8
9
10	Memory Management	userheapAlloc	Adress	size_t	Allocates memory for the userheap with the specified size returning the adress to the beginning of this area
11		userheapFree		Adress, size_t	Frees Userheap beginning at Adress with the specified size
12
13
14
15	File	fopen	file-struct*	Path, mode (const char*)	Like in C standard library
16		fgetc	char		Like in C standard library
17		fputc	error		Like in C standard library
18		fseek	error		Like in C standard library
19		fflush	error		Like in C standard library
20		fmove	error		If destination is 0, the file is removed, otherwise its moved from source to destination. The function allows movement between different partitions
21		fclose	error		Like in C standard library
22		partition_format	error	Path (char*), FS_t, name (char*)	Takes the path, the desired filesystem type and name and formats the partition
23
24
25	IPC	ipc_getString	char*	Path (char*)	Returns a string from the IPC-tree
26		ipc_setString	Success (bool)	Path (char*), const char*	Fills in a string to the IPC-tree
27		ipc_getInt	int64_t	Path (char*)	Returns an Integer from the IPC-tree (64-bit)
28		ipc_setInt	Success (bool)	Path (char*), int64_t	Fills in an Integer to the IPC-tree (64-bit)
29		ipc_getDouble	double	Path (char*)	Returns a double precision floating point number from the IPC-tree
30		ipc_setDouble	Success (bool)	Path (char*), double	Fills in a double precision floating point number to the IPC-tree
31		ipc_deleteKey	Success (bool)	Path (char*)	Deletes a value from the IPC-tree
32		ipc_allowAccess	Success (bool)	?	Allows a task/user to access that key
33
34
35
36
37
38		enableEvents		bool	Informs the OS, wheter we will handle events or not. Default is false.
39		pollEvent	Type (uint32_t)	Buffer (void**)	Returns the first event from the event queue and stores the data in the given buffer. If the length of the data exeeds its bounds, the function returns 1. If no event is available, it returns 0.
40	Getting information quickly	getCurrentMilliseconds	uint64_t		Returns the time elapsed since boot in milliseconds
41
42
43
44
45
46
47
48
49
50	System control	systemControl		SYSTEM_CONTROL (enum)	Advices the system to do something (Reboot, etc.)
51		systemRefresh		SYSTEM_INFO (enum)	Makes the system refreshing the specified Information
52
53
54
55	Graphics	putch		char	Prints a character to the screen at the cursors position
56		textColor		uint8_t (color)	Sets the color of the following text output
57		setScrollfield		Top, bottom	Sets the borders of the scrolling area
58		setCursor		Position	Sets the position of the write cursor
59		getCursor		Position*	Writes the position of the write cursor to the given address.
60		readChar	char	Position	Reads a char from the userscreen at the specified position
61		clearScreen		uint8_t (color)	Clears the userscreen
62
63
64
65
66
67
68
69
70	User input
71		keyPressed	bool	Key (enum)	Returns true if the specified key is pressed
72		mousePressed	bool	Mousebutton (enum)	Returns true If the specified button is pressed
73		getMousePosition	Position		Returns the position of the mouse cursor
74		setMousePosition		Position	Sets the position of the mouse cursor
75
76
77
78
79
80	Sound	beep		Frequency, duration	Beeps with the specified frequency for duration in milliseconds
81
82
83
84
85	Network	tcp_connect	ID (uint32_t)	IP, port
86		tcp_send		ID, data, length
87		tcp_close		ID
88
89
90